Dirty Mike and the Boys

Programmers Manual
R1

Group Members
Kristopher Pepper
Jeremy Smith
Arif Mohammad
Jacob Culley

Table of Contents
strlen…………………………………………………………………………………………………….3
strcpy……………………………………………………………………………………………………3
atoi………………………………………………………………………………………………………4
strcmp…………………………………………………………………………………………………...4
strcat……………………………………………………………………………………………………..5
ispace…………………………………………………………………………………………………….5
memset………………………………………………………………………………………………….6
strok……………………………………………………………………………………………………..6
version………………………………………………………………………………………………….7
getTime………………………………………………………………………………………………….8
getDate…………………………………………………………………………………………………8
bcdToDecimal…………………………………………………………………………………………9
commandHandler……………………………………………………………………………………….10

Strlen()
Takes in a string and returns the length of the string.
int strlen(const char *s)
{
int length;
for (length = 0; *s != '\0'; s++)
{
length++;
}
return(length);
}

Parameter: s-input string

Return: length of the string as an int

stcpy()

Takes in two strings and replaces the first with the second.

char* strcpy(char *s1, const char *s2)
{
int i = 0;
while (s2[i] != '\0')
{
s1[i] = s2[i];
i++;
}
s1[i] = '\0';
return(s1); // return pointer to destination string

}

Parameters: s1-destination string, s2-source string

Return: pointer to copied string

atoi()

Takes a string and converts it to its integer equivalent.

int atoi(const char *s)
{
int result = 0;
 int i;
    for (i = 0; s[i] != '\0'; ++i)
{
        result = result*10 + s[i] - '0';
  }
    // return result.
    return result; // return integer
}

Parameter: s-input string

Return: integer equivalent of the input string

strcmp()a

 Compares two strings, showing which is longer or if they are equal.

int strcmp(const char *s1, const char *s2)
{
while ( *s1 != '\0' && *s2 != '\0' )
      {
        if ( *s1 != *s2 )
{
   break;
}
s1++;
s2++;
      }
return ( *(unsigned char *)s1 - *(unsigned char *)s2 );
}

Parameters: s1-string 1 s2-string 2

Return: the comparison status of the two strings

strcat()

Combines two strings into one.

char* strcat(char *s1, const char *s2)
{
  char *rc = s1;
  if (*s1) while(*++s1);
  while( (*s1++ = *s2++) );
  return rc;
}

Parameter: s1-destination string, s2-source string

Return: one string, s1 followed by s2.

isspace()

Determines if the inputted character is empty

int isspace(const char *c)
{
  if (*c == ' ' ||
      *c == '\n' ||
      *c == '\r' ||
      *c == '\f' ||
      *c == '\t' ||
      *c == '\v'){
    return 1;
  }
  return 0;
}

Parameter: c- character

Return: 1 if empty character 0 if not.

memset()

Sets a region of memory

void* memset(void *s, int c, size_t n)
{
  unsigned char *p = (unsigned char *) s;
  while(n--){
    *p++ = (unsigned char) c;
  }
  return s;
}

Parameters: s-destination, c-byte to write, n-count

Returns: pointer to memory

strtok()

Breaks up a string into smaller pieces

char* strtok(char *s1, const char *s2)
{
  static char *tok_tmp = NULL;
  const char *p = s2;

  //new string
  if (s1!=NULL){
    tok_tmp = s1;
  }
  //old string cont'd
  else {
    if (tok_tmp==NULL){
      return NULL;
    }
    s1 = tok_tmp;
  }

  //skip leading s2 characters
  while ( *p && *s1 ){
    if (*s1==*p){
      ++s1;
      p = s2;
      continue;
    }
    ++p;
  }

  //no more to parse
  if (!*s1){
    return (tok_tmp = NULL);
  }

  //skip non-s2 characters
  tok_tmp = s1;
  while (*tok_tmp){
    p = s2;
    while (*p){
      if (*tok_tmp==*p++){
*tok_tmp++ = '\0';
return s1;
      }
    }
    ++tok_tmp;
  }

  //end of string
  tok_tmp = NULL;
  return s1;
}

Parameters: s1-string, s2-delimiter

Returns: last character from smaller strings

version()

Prints out a string which says what module the OS is on and another string that says when it was completed

version(){
serial_println("R1");
  serial_println("2/4/2016");
}

Parameters: none

Returns: none

getTime()

Prints out the time that is stored on the registry.

void getTime(){
outb(0x70,0x04);
unsigned char hours= inb(0x71);
 bcdToDecimal(hours);
serial_print(":");
outb(0x70,0x02);
unsigned char minutes=inb(0x71);
bcdToDecimal(minutes);
serial_print(":");
outb(0x70,0x00);
unsigned char seconds=inb(0x71);
bcdToDecimal(seconds);
}

Parameters: none

Returns: prints out the current time

getDate()

Prints out the date that is currently stored on the registry.

void getDate(){
outb(0x70,0x08);
unsigned char months= inb(0x71);
 bcdToDecimal(months);
serial_print("/");
outb(0x70,0x07);
unsigned char days=inb(0x71);
bcdToDecimal(days);
serial_print("/");
outb(0x70,0x09);
unsigned char years=inb(0x71);
bcdToDecimal(years);
}

Parameters: none

Returns: prints out the current date.

bcdToDecimal()

Converts a given binary number to decimal

void bcdToDecimal(unsigned char n)
{
int ones1, tens1;
unsigned char tens=((n & 0xF0) >>4) *10;
unsigned char ones=(n & 0x0F);

tens1= tens+0x30;
ones1= ones+0x30;
while(tens1 >57)
tens1=tens1-9;

serial_print((const char *)&tens1);
serial_print((const char *)&ones1);

}

Parameters: take in an unsigned char.

Return: none

setTime()

Takes in 3 inputs for hours, minutes, and seconds and adds those values to their appropriate registry and saves them.

void setTime(int hours, int minutes, int seconds ){
int h= decimalToBcd(hours);
cli();
outb(0x04,h);
outb(0x71,0x04);
sti();
int m= decimalToBcd(minutes);
cli();
outb(0x02,m);
outb(0x71,0x02);
sti();
int s= decimalToBcd(seconds);
cli();
outb(0x00,s);
outb(0x71,0x00);
}

Parameters: int hours, int minutes, int seconds

Returns: none

setDate()

Takes in 3 inputs for months, days, and years and adds those values to their appropriate registry and saves them.
void setDate(int months, int days, int years)
{
unsigned char m= decimalToBcd(months);
unsigned char d= decimalToBcd(days);
unsigned char y= decimalToBcd(years);
}
Parameters: int months, int days, int years

Returns: none

commandHandler()

Accepts input and deals with commands accordingly.